## Slide 1
GRCR-Net: A Complex Residual Network with GPR Denoising and Rotational Augmentation for Automatic Modulation Classification A Breakthrough Approach for AMC
Junkai Li
College of Information Engineering Zhejiang University of Technology
July 5, 2025
Junkai Li (ZJUT)
July 5, 2025 1 / 29
GRCR-Net

## Slide 2
1 Background and Challenges
2 GRCR-Net Innovation Overview
3 Core Technical Innovations
4 Experimental Results and Analysis
5 Technical Contributions and Impact
6 Conclusion and Future Work
Junkai Li (ZJUT) GRCR-Net July 5, 2025 2 / 29
Outline

## Slide 3
Critical Applications:
Cognitive Radio: Dynamic spectrum sensing and management
Spectrum Monitoring: Radio environment situational awareness
Military Communications: Electronic warfare and signal intelligence
5G/6G Networks: Intelligent signal processing
Key Challenge:
Accurate classification under low Signal-to-Noise Ratio (SNR)
Preserving I/Q signal phase information
The Importance of Automatic Modulation Classification
Robust performance in complex electromagnetic
envi rJ nkmai in(tZsJUT) GRCR-Net July 5, 2025 3 / 29
Military Comm
Cognitive Radio
Spectrum Monitor
5G/6G
AMC

## Slide 4
Limitations of Existing Methods:
Likelihood-based methods: High computational complexity
Feature-based methods: Rely on expert knowledge
Deep learning methods: Severe performance drop in low SNR
Critical Issues:
Noise severely affects signal quality
Loss of I/Q signal phase information
Data imbalance and poor generalization
 |  |  | GR | CR-Net
Core Challenge: Performance Degradation in Low SNR
Junkai Li (ZJUT) GRCR-Net July 5, 2025 4 / 29
−20 −10 0 10 20
SNR (dB)
100
80
60
40
20
Accuracy (%)
aseline
B

## Slide 5
Power Analysis: Visual Understanding
Understanding Power Relationships
Junkai Li (ZJUT) GRCR-Net July 5, 2025 5 / 29

## Slide 6
Extreme Low SNR Challenge:
At SNR = -20dB: Psignal = 1%, Pnoise = 99% Previous SOTA methods: only ~60% accuracy Massive noise severely degrades classification
Traditional denoising methods fail
Our Solution: Adaptive GPR Denoising
Model signal as Gaussian Process
Assume Additive White Gaussian Noise (AWGN) Derive noise power from signal statistics
The Challenge: Extreme Noise Conditions
Adaptive scale parameters for different SNRs
Junkai Li (ZJUT) GRCR-Net July 5, 2025 6 / 29
SNR = -20dB: Signal Power Only 1%, Noise 99%
Signal 1% Noise 99% Denoised
SNR = -20dB
GPR

## Slide 7
From 99% Noise to Actionable Intelligence
The Core Question:
Why tackle a problem where signals are 99% noise?
Critical Real-World Scenarios:
1. Military Reconnaissance: Enemy communications are intentionally weak to evade detection. Just knowing "something is there" provides critical intelligence for strategic decisions.
2. Deep Space Communication: Probe signals, after traveling billions of kilometers through cosmic noise, arrive incredibly faint on Earth. We must recover them from the void to maintain contact.
3. Harsh Environment Degradation: Normal signals passing through dense buildings or
strong interference become temporarily buried in noise. The connection must be
maintained.
Junkai Li (ZJUT) GRCR-Net July 5, 2025 7 / 29
Why Tackle the Impossible? The Value in the Noise

## Slide 8
Two-Step Approach to Tackle the Impossible
Our Unified Strategy:
Step 1: Build a noise-robust model that can extract weak signals → OUR WORK
Step 2: Long-term integration of thousands of weak results → HIGH CONFIDENCE
Our Contribution: GRCR-Net - A breakthrough noise-robust model Achievement: Extract signals from noise with 65.38% accuracy Impact: Enabling detection where others see only noise
Step 1 is the focus of this work - Building the noise-robust model!
Junkai Li (ZJUT) GRCR-Net July 5, 2025 8 / 29
Our Unified Strategy: From Noise to Intelligence

## Slide 9
Final Performance: 65.38% Accuracy,
Surpassing State-of-the-Art
Junkai Li (ZJUT) GRCR-Net July 5, 2025 9 / 29
GRCR-Net: Three Core Innovations
GRCR-Net Hybrid Architecture
Rotational Augmentation Geometric Symmetry
Hybrid Architecture ComplexCNN +ResNet
GPR Denoising Adaptive Noise Suppression
+5.86%
+3.78%
56.94%

## Slide 10
Part I: Signal Model and Assumptions
Core Assumptions:
1 Additive White Gaussian Noise (AWGN):
r[n] = s[n] + w[n] (1)
2 Independent Gaussian Distribution: Each noise sample is independent and follows Gaussian distribution
wI[n], wQ[n] ~ N(0,σ ) (I/Q components) (2)
3 Gaussian Process Modeling: The entire signal can be modeled as a Gaussian Process
w[n] ~ CN(0,σ ) (Complex AWGN) (3)
With these assumptions, we can derive the optimal noise estimation!
Junkai Li (ZJUT) GRCR-Net July 5, 2025 10 / 29
n
2
n
2
GPR Denoising: Theoretical Foundation

## Slide 11
2. SNR Power Ratio:
SNR linear = 10SNR dB/10
3. Noise Power Calculation:
GPR Denoising: Mathematical Derivation Process
Junkai Li (ZJUT) GRCR-Net July 5, 2025 11 / 29
Step-by-Step Derivation:
1. I/Q Power Calculation:
Part II: Complete Derivation Process
(4)
(5)
(6)

## Slide 12
Step 4: Estimate Noise Standard Deviation from Gaussian Distribution
Since noise follows Gaussian distribution, for complex AWGN:
Pw = E[|w[n]| 2] = E[wI2 [n]] + E[w [n]] = 2σ (8)
Therefore, the noise variance for each component:
Final Noise Standard Deviation:
(10)
n
2
Q
2
GPR Denoising: Final Noise Estimation
Key Insight: This σ becomes the noise variance parameter α in our GPR model, enabling theoretically grounded denoising!
n
2
Junkai Li (ZJUT) GRCR-Net July 5, 2025 12 / 29

## Slide 13
RBF Kernel Function:
(11)
Length Scale L Controls Smoothing Strength:
Large L → Strong smoothing, risk of oversmoothing
Small L → Weak smoothing, preserves signal details
Problems with Fixed Large L at Low SNR:
1 Oversmoothing of signal features
2 Loss of time-domain details
3 Loss of critical phase information
Our Adaptive Strategy:
Key Insight: Lower SNR → Smaller L → Preserve more signal details !
Junkai Li (ZJUT) GRCR-Net July 5, 2025 13 / 29
GPR Denoising: Adaptive Length Scale Strategy

## Slide 14
1 Power Estimation:
Pr =
2 Noise Variance: σ = 2(10SN 10 +1)
3 Adaptive Length Scale:
L = max(Lmin, L0(1 + SNR/20))
4 GPR Denoising: Apply to I and Q components separately
5 Signal Reconstruction: [n] = I[n] + j Q[n]
Key Advantages:
Theoretically grounded noise estimation SNR-adaptive smoothing control
Preserves signal feature integrity
Optimal for different noise conditions
Junkai Li (ZJUT) GRCR-Net
ˆ
s
ˆ
s
ˆ
s
/
r
R
P
n
2
Innovation 1: Complete GPR Denoising Pipeline
Complete Algorithm:
Result: +5.86% Accuracy Improvement
July 5, 2025 14 / 29

## Slide 15
Theoretical Foundation:
Rotational symmetry of digital modulation
constellations
Mathematical rigor of complex plane
rotation
Exploitation of phase invariance
Implementation:
(13)
Augmentation Strategy:
90。, 180。, 270。rotations
4× training data expansion
Applied to symmetric modulation types
Junkai Li (ZJUT) GRCR-Net July 5, 2025 15 / 29
Innovation 2: Geometric Symmetry-Based Rotational Augmentation

## Slide 16
Design Principles:
Complex Domain Processing: Direct I/Q signal handling, preserving phase information Residual Learning: Solving gradient vanishing in deep networks
ModReLU Activation: Maintaining complex geometric structure
Lightweight Design: Balancing performance and computational efficiency
Junkai Li (ZJUT) GRCR-Net July 5, 2025 16 / 29
Complex Pool
Innovation 3: Hybrid ComplexCNN-ResNet Architecture
Lightweight Hybrid Complex-ResNet Architecture Multi-Layer Residual Blocks with Direct Skip Connections
+
Complex Domain Processing Real Domain Classification
+
skip
skip
skip
ComplexConv1D
256 filters (s=2)
ComplexConv1D
128 filters (s=2)
Permute (128,2)
ComplexConv1D
32 filters,
k=5
Model: 400K parameters — 4 processing stages
— Simple residual skip connections
Complex BN
Activation
ComplexConv1D
128 filters
(64,64)
ComplexConv1D
64 filters
Complex BN
Activation
ComplexConv1D
64 filters
Complex BN
Activation
ComplexConv1D
256 filters
Complex BN
Activation
ComplexConv1D
256 filters
Complex BN
Complex Global Avg Pool
Dense
Softmax 11 classes
Complex
Dense
512 units
Complex BN
Complex
Leaky
ReLU
Complex
Leaky
ReLU
Complex Magnitude
Dense 256 ReLU
Complex BN
Complex BN
Dropout 0.3
Dropout 0.5
→ Direct Skip Connection
I/Q Radio Signals
11 Modulation Classes
Input (2,128)
— Complex Flow
Residual Addition
— Real Flow
+
+

## Slide 17
RML2016.10a Dataset:
11 modulation types
SNR range: -20dB to +18dB
128 complex samples per signal Data split: 72%/8%/20%
Experimental Environment:
Intel Core i9-13900K
NVIDIA GeForce RTX 4090 (24GB) TensorFlow 2.17.0 + Keras 3.6.0
Ubuntu 24.04.2 LTS
Dataset and Experimental Setup
Modulation | Samples
8PSK | 22,000
AM-DSB | 22,000
AM-SSB | 22,000
BPSK | 22,000
CPFSK | 22,000
GFSK | 22,000
PAM4 | 22,000
QAM16 | 22,000
QAM64 | 22,000
QPSK | 22,000
WBFM | 22,000
Junkai Li (ZJUT) GRCR-Net July 5, 2025 17 / 29

## Slide 18
Key Findings:
ComplexCNN shows natural advantage for
I/Q signals
Model Architecture Accuracy (%) ResNet’s residual connections improve
FCNN 42.65 training stability
CNN2D 47.31 GRCR-Net achieves 8.27%
Transformer 47.86 improvement over best baseline
CNN1D 54.94
ResNet 55.37 Performance Breakthrough:
ComplexCNN 57.11 Surpasses existing SOTA methods
GRCR-Net 65.38 Consistent improvement across all SNR
conditions
Exceptional performance in low SNR
environments
Junkai Li (ZJUT) GRCR-Net July 5, 2025 18 / 29
Baseline Model Performance Comparison

## Slide 19
 | Baseline Performance Data Augmentation Contribution GPR Denoising Contribution | 
65.38% |  | 
62.80% |  | 
60.72% |  | 
56.94% |  | 
Key Insights:
GPR denoising contributes most: +5.86 percentage points
Rotational augmentation provides stable improvement: +3.78 percentage points
Synergistic effect of both techniques: total improvement of 8.44 percentage points
Junkai Li (ZJUT) GRCR-Net July 5, 2025 19 / 29
Ablation Study: Component Contribution Analysis
Hybrid Model + Data Augmentation + GPR Denoising + Complete Solution
Technical Configuration
70.0
67.5
65.0
62.5
60.0
57.5
55.0
52.5
50.0
Ablation Study: Cumulative Contribution Analysis of Technical Components
C lass if icat ion Accuracy (%)

## Slide 20
 | ResNet CNN1D |  |  |  |  |  |  |  | 
 | Hybrid Hybrid+G | PR+Aug |  |  |  |  |  |  | 
 |  | -10 | dB |  |  | 10 |  | dB |  |  | 
 |  |  |  |  |  |  |  | ResNet CNN1D Complex Hybrid Hybrid+ |  | CNN GPR+Aug | 
Performance Across Different SNR Conditions
GPR Denoising Performance Analysis
July 5, 2025 20 / 29
Junkai Li (ZJUT)
GRCR-Net
-20.0 -17.5 -15.0 -12.5 -10.0 -7.5 -5.0 -2.5
Signal-to-Noise Ratio (dB)
-20 -15 -10 -5 0 5 10 15
Signal-to-Noise Ratio (dB)
Low SNR Performance Detailed Comparison
40
35
30
25
20
15
10
5
0
60
40
20
0
Model Performance vs SNR
Classification Accuracy (%)
Classification Accuracy (%)
100
80
ComplexCNN
0dB

## Slide 21
Key Findings:
Low SNR (-20 to -8dB):
Peak: +14.90% at -10dB
Average: 7.25%
Medium SNR (-6 to 4dB):
Range: 3.74% to 6.82%
Average: 5.12%
High SNR (6 to 18dB):
Range: 3.50% to 5.93%
Average: 5.07%
SNR | Base | +GPR | Gain
-20 | 8.93 | 9.96 | +1.03
-18 | 8.68 | 10.22 | +1.54
-16 | 9.85 | 12.69 | +2.84
-14 | 11.08 | 17.32 | +6.24
-12 | 12.65 | 24.18 | +11.53
-10 | 20.15 | 35.05 | +14.90
-8 | 34.66 | 47.36 | +12.70
-6 | 54.86 | 61.21 | +6.35
-4 | 64.02 | 70.84 | +6.82
-2 | 75.66 | 80.89 | +5.23
0 | 79.43 | 83.17 | +3.74
2 | 82.96 | 87.07 | +4.11
4 | 84.56 | 89.00 | +4.44
6 | 83.93 | 89.38 | +5.45
8 | 83.17 | 89.10 | +5.93
10 | 84.73 | 89.85 | +5.12
12 | 85.81 | 90.31 | +4.50
14 | 85.31 | 88.81 | +3.50
16 | 82.25 | 88.15 | +5.90
18 | 83.87 | 88.98 | +5.11
Detailed SNR Performance Analysis
Best Performance: +14.90% improvement
Junkai Li (ZJUT) GRCR-Net July 5, 2025 21 / 29

## Slide 22
0.70
0.60
0.50
0.40
0.30
0.20
0.10
0.000 20 40 60 80 100
Key Insights:
Fast Convergence: Optimal in 5-10 epochs
Stable Training: Smooth without oscillations
Best Performance: Outperforms all baselines
Robust Results: Consistent across
runs
Training Convergence Analysis
Training Advantage: Fast & Stable Convergence
Junkai Li (ZJUT) GRCR-Net July 5, 2025 22 / 29
CNN2D
CNN1D
Transformer
ResNet
Complex NN
Hybrid
GRCR-Net (Proposed)
Validation Accuracy Convergence Curves
Val idat ion Accuracy
Training Epochs

## Slide 23
1 Adaptive Noise Suppression Technology
First SNR-adaptive GPR denoising algorithm
Optimal denoising under different noise conditions
Novel approach for complex electromagnetic environments
2 Geometric Property Data Augmentation Strategy
Exploits inherent symmetry of modulation signals
Significantly improves robustness to phase offset
Effective solution for data-scarce scenarios
3 Hybrid Neural Network Architecture Innovation
First fusion of ComplexCNN and ResNet advantages
Deep residual learning in complex domain
New architectural paradigm for I/Q signal processing
Junkai Li (ZJUT) GRCR-Net July 5, 2025 23 / 29
Major Technical Contributions

## Slide 24
Core Advantages:
Performance Leadership: Surpasses best existing method by 0.79%
Technical Innovation: Organic fusion of three core technologies
Practical Robustness: Stable performance in complex environments
Scalability: Components can be applied independently
Junkai Li (ZJUT) GRCR-Net July 5, 2025 24 / 29
Method | Accuracy(%) | Year | Publication | Model Size | Key Technology
LDCVNN | 62.41 | 2025 | JCR Q2 | Lightweight | Dual-branch complex network
ULCNN | 62.47 | 2022 | JCR Q2 | Lightweight | Ultra-lightweight CNN
AMC-NET | 62.51 | 2023 | ICASSP (CCF B) | Normal | Frequency-domain denoising
HFECNET-CA | 63.92 | 2023 | JCR Q2 | Lightweight | Attention mechanism
AbFTNet (Previous SOTA) | 64.59 | 2024 | JCR Q2 | Normal | Multimodal fusion
GRCR-Net (Ours) | 65.38 | 2025 | This Work | Lightweight | GPR+Rotation+Hybrid
Comparison with State-of-the-Art Methods

## Slide 25
65.38% accuracy
+0.79% vs. AbFTNet (2024) +2.87% vs. AMC-NET (2023)
+2.91% vs. ULCNN (2022) Key Advantages:
Clear performance leadership
Consistent improvements
Robust across conditions
New benchmark established
Comprehensive Performance Comparison
Junkai Li (ZJUT) GRCR-Net July 5, 2025 25 / 29
New SOTA 65.38%
SOTA Achievement:

## Slide 26
Impact Significance:
• Solution for complex electromagnetic environments
• Advancement of cognitive radio technology
• New insights for signal processing field
• Important theoretical and practical value
Open Source Contribution:
• Complete code open-sourced
• Detailed experimental data
• Comprehensive technical documentation
Core Achievements:
√ Achieved 65.38% classification accuracy √ Surpassed existing SOTA methods
√ Exceptional performance in low SNR environments
√ Proposed three core technical innovations
Technical Breakthroughs:
• Adaptive GPR denoising algorithm
• Geometric symmetry data augmentation
• Hybrid ComplexCNN-ResNet architecture
Research Summary
Junkai Li (ZJUT) GRCR-Net July 5, 2025 26 / 29
GRCR-Net: A Breakthrough AMC Method

## Slide 27
1 Algorithm Optimization and Extension
Explore performance in more complex channel environments
Research real-time processing optimization strategies
Extend to more modulation types
2 Technology Fusion and Innovation
Combine with emerging architectures like Transformers
Explore multimodal signal fusion
Research self-supervised learning methods
3 Practical Deployment and Applications
Hardware acceleration and edge computing optimization
Large-scale real-environment validation
Industrial application promotion
Junkai Li (ZJUT) GRCR-Net July 5, 2025 27 / 29
Future Research Directions

## Slide 28
Thank You!
Questions and Discussion Welcome
Open Source Repository:
https://github.com/LJK666666666/radioML-v3
Junkai Li (ZJUT) GRCR-Net July 5, 2025 28 / 29