## Slide 1: GRCR-Net: A Complex Residual Network with GPR Denoising and Rotational Augmentation for Automatic Modulation Classification
A Breakthrough Approach for AMC
Junkai Li
College of Information Engineering Zhejiang University of Technology
July 5, 2025
GRCR-Net

## Slide 2: Outline
1
Background and Challenges
2
GRCR-Net Innovation Overview
Core Technical Innovations
Experimental Results and Analysis
5
Technical Contributions and Impact
6
Conclusion and Future Work
GRCR-Net

## Slide 3: The Importance of Automatic Modulation Classification
Critical Applications:
Cognitive Radio: Dynamic spectrum sensing and management
Spectrum Monitoring: Radio environment situational awareness
Military Communications: Electronic warfare and signal intelligence
5G/6G Networks: Intelligent signal processing
Key Challenge:
Accurate classification under low Signal-to-Noise Ratio (SNR)
Preserving I/Q signal phase information
Robust performance in complex electromagnetic
AMC
Cognitive Radio
Spectrum
Monitor
Military Comm
5G/6G
environments
GRCR-Net

## Slide 4: Core Challenge: Performance Degradation in Low SNR
Limitations of Existing Methods:
Likelihood-based methods: High computational complexity
Feature-based methods: Rely on expert knowledge
Deep learning methods: Severe performance drop in low SNR
Critical Issues:
Noise severely affects signal quality Loss of I/Q signal phase information Data imbalance and poor generalization
−20 −10
20
40
100
80
60
0
SNR (dB)
Accuracy (%)
Baseline GRCR-Net
10 20
GRCR-Net

## Slide 5
Power Analysis: Visual Understanding
Understanding Power Relationships
GRCR-Net

## Slide 6: The Challenge: Extreme Noise Conditions
SNR = -20dB: Signal Power Only 1%, Noise 99%
Extreme Low SNR Challenge:
At SNR = -20dB: Psignal = 1%, Pnoise = 99% Previous SOTA methods: only ∼60% accuracy Massive noise severely degrades classification Traditional denoising methods fail
Our Solution: Adaptive GPR Denoising
Model signal as Gaussian Process
Assume Additive White Gaussian Noise (AWGN) Derive noise power from signal statistics Adaptive scale parameters for different SNRs
Signal 1%
Noise 99%
SNR = -20dB
GPR
Denoised
GRCR-Net

## Slide 7: Why Tackle the Impossible? The Value in the Noise
From 99% Noise to Actionable Intelligence
The Core Question:
Why tackle a problem where signals are 99% noise?
Critical Real-World Scenarios:
Military Reconnaissance: Enemy communications are intentionally weak to evade detection. Just knowing "something is there" provides critical intelligence for strategic decisions.
Deep Space Communication: Probe signals, after traveling billions of kilometers through cosmic noise, arrive incredibly faint on Earth. We must recover them from the void to maintain contact.
Harsh Environment Degradation: Normal signals passing through dense buildings or strong interference become temporarily buried in noise. The connection must be maintained.
GRCR-Net
10 / 29

## Slide 8: Our Unified Strategy: From Noise to Intelligence
Two-Step Approach to Tackle the Impossible
Our Unified Strategy:
Step 1: Build a noise-robust model that can extract weak signals → OUR WORK
Step 2: Long-term integration of thousands of weak results → HIGH CONFIDENCE
Our Contribution: GRCR-Net - A breakthrough noise-robust model Achievement: Extract signals from noise with 65.38% accuracy Impact: Enabling detection where others see only noise
Step 1 is the focus of this work - Building the noise-robust model!
GRCR-Net
10 / 29

## Slide 9: GRCR-Net: Three Core Innovations
GRCR-Net Hybrid Architecture
GPR
Denoising
Adaptive Noise Suppression
Rotational Augmentation
Geometric Symmetry
Hybrid Architecture
ComplexCNN
+ResNet
+5.86%
+3.78%
56.94%
Final Performance: 65.38% Accuracy, Surpassing State-of-the-Art
GRCR-Net
10 / 29

## Slide 10: GPR Denoising: Theoretical Foundation
Part I: Signal Model and Assumptions
Core Assumptions:
1
Additive White Gaussian Noise (AWGN):
r [n] = s[n] + w [n]
Independent Gaussian Distribution: Each noise sample is independent and follows Gaussian distribution
(1)
2
n
wI [n], wQ [n] ∼ N (0, σ2) (I/Q components) (2)
3
Gaussian Process Modeling: The entire signal can be modeled as a Gaussian Process
w [n] ∼ CN (0, σ2) (Complex AWGN) (3)
n
With these assumptions, we can derive the optimal noise estimationỊ
GRCR-Net
10 / 29

## Slide 11: GPR Denoising: Mathematical Derivation Process
Part II: Complete Derivation Process
Step-by-Step Derivation:
1. I/Q Power Calculation:
r
P =
1
M
M−1
Σ
k=0
2
(r [k] + r
I Q
2
[k] ) (4)
(5)
SNR Power Ratio:
SNRlinear = 10SNRdB/10
Noise Power Calculation:
Pr
P =
(6)
4. Gaussian Noise Estimation
:
w
10SNRdB/10 + 1
GRCR-Net

## Slide 12: GPR Denoising: Final Noise Estimation
Step 4: Estimate Noise Standard Deviation from Gaussian Distribution
Since noise follows Gaussian distribution, for complex AWGN:
Pw = E[|w [n]|2] = E[w 2[n]] + E[w 2 [n]] = 2σ2
I Q n
Therefore, the noise variance for each component:
(8)
2
n
σ = =
P P
w r
2 2(10SNRdB/10 + 1)
(9)
σ
n
Final Noise Standard Deviation:
s
=
Pr
2(10SNRdB/10 + 1)
(10)
Key Insight: This σ2 becomes the noise
n
variance parameter α in our GPR model,
enabling theoretically grounded denoising!
GRCR-Net

## Slide 13: GPR Denoising: Adaptive Length Scale Strategy
RBF Kernel Function:
2
(x − x )
2
i j
2L2
k(xi, xj ) = σf exp −
Length Scale L Controls Smoothing Strength:
(11)
Large L → Strong smoothing, risk of oversmoothing Small L → Weak smoothing, preserves signal details
Problems with Fixed Large L at Low SNR:
Oversmoothing of signal features Loss of time-domain details
Loss of critical phase information
1
2
3
Our Adaptive Strategy:
L =
(
L
0
if SNR ≥ 0 dB if SNR < 0 dB
max(Lmin, L0(1 + SNR/20))
(12)
Key Insight: Lower SNR → Smaller L → Preserve more signal details!
GRCR-Net

## Slide 14: Innovation 1: Complete GPR Denoising Pipeline
Complete Algorithm:
1
Power Estimation:
r
P =
1
M
Σ
M−1
k=0
I
2
(r [k] + r
Q
2
[k] )
2
2
n
Noise Variance: σ =
P
r
2(10SNR/10+1)
3
Adaptive Length Scale:
L = max(Lmin, L0(1 + SNR/20))
GPR Denoising: Apply to I and Q components separately
Signal Reconstruction: sˆ[n] = sˆI [n] + jsˆQ [n]
4
5
Key Advantages:
Theoretically grounded noise estimation SNR-adaptive smoothing control Preserves signal feature integrity
Result: +5.86% Accuracy Improvement
Optimal for different noise conditions
Junkai Li (ZJUT)
GRCR-Net

## Slide 15: Innovation 2: Geometric Symmetry-Based Rotational Augmentation
Theoretical Foundation:
Rotational symmetry of digital modulation constellations
Mathematical rigor of complex plane rotation
Exploitation of phase invariance
Implementation:
′
I
s [n]
Q
s′ [n]
=
I
cos θ − sin θ s [n] sin θ cos θ sQ [n]
(13)
Augmentation Strategy:
90°, 180°, 270° rotations 4× training data expansion
Applied to symmetric modulation types
GRCR-Net
15 / 29

## Slide 16: Innovation 3: Hybrid ComplexCNN-ResNet Architecture
Real Domain Classification
(128,2) k=5
ComplexConv1CDomplex
ComplexLeaky
Permut3e2 filters, BN ReLU
64 filtersBN 64 filters
Complex Pool
ComplexCompleCxComonpvle1xD
(64,6C4o)mplexConAvc1tDivation BN
ComplexConv1D
(s=2) BN
ComplexComplexConv1D
128 filters Acti1v2a8tifiolntersBN
BN
Complex(s=2)
256 filters Acti2v5a6tifiolnterBs N 256 filters
ComplexCompleCxoCmopnAlvec1xtDivation BN Global
Dense Leaky
Avg Pool 512 units ReLU
0.5
ComplexConv1D ComplexCCoomnpvl1eCDxomplex ComplexComplexDropoutComplex Dense 256Dropout Dense
Softmax
Magnitude ReLU 0.3
11 classes
skip
+
skip
+
skip
+
Lightweight Hybrid Complex-ResNet Architecture
Multi-Layer Residual Blocks with Direct Skip Connections Complex Domain Processing
I/Q Radio Signals
Input (2,128)
11 Modulation Classes
→ Direct Skip Connection
Model: 400K parameters — 4 processing stages — Simple residual skip connections
— Complex Flow — Real Flow
+ Residual Addition
Design Principles:
Complex Domain Processing: Direct I/Q signal handling, preserving phase information
Residual Learning: Solving gradient vanishing in deep networks ModReLU Activation: Maintaining complex geometric structure Lightweight Design: Balancing performance and computational efficiency
GRCR-Net

## Slide 17: Dataset and Experimental Setup
RML2016.10a Dataset:
11 modulation types
SNR range: -20dB to +18dB 128 complex samples per signal Data split: 72%/8%/20%
Experimental Environment:
Intel Core i9-13900K
NVIDIA GeForce RTX 4090 (24GB)
TensorFlow 2.17.0 + Keras 3.6.0
Ubuntu 24.04.2 LTS
Modulation | Samples
8PSK | 22,000
AM-DSB | 22,000
AM-SSB | 22,000
BPSK | 22,000
CPFSK | 22,000
flFSK | 22,000
PAM4 | 22,000
QAM16 | 22,000
QAM64 | 22,000
QPSK | 22,000
WBFM | 22,000
GRCR-Net

## Slide 18: Baseline Model Performance Comparison
Model Architecture
Accuracy (%)
FCNN CNN2D
Transformer CNN1D
ResNet ComplexCNN
42.65
47.31
47.86
54.94
55.37
57.11
GRCR-Net
65.38
Key Findings:
ComplexCNN shows natural advantage for I/Q signals
ResNet’s residual connections improve training stability
GRCR-Net achieves 8.27% improvement over best baseline
Performance Breakthrough:
Surpasses existing SOTA methods
Consistent improvement across all SNR conditions
Exceptional performance in low SNR environments
GRCR-Net

## Slide 19: Ablation Study: Component Contribution Analysis
Hybrid Model
+ Data Augmentation
+ GPR Denoising
+ Complete Solution
Technical Configuration
50.0
52.5
55.0
57.5
60.0
62.5
65.0
67.5
70.0
Classification Accuracy (%)
Ablation Study: Cumulative Contribution Analysis of Technical Components
Baseline Performance Data Augmentation Contribution GPR Denoising Contribution |  |  |  |  |  | 
 |  |  |  |  | 65.38% | 
62.80% |  |  |  |  |  | 
60.72% |  |  |  |  |  | 
56.94% |  |  |  |  |  | 
Key Insights:
GPR denoising contributes most: +5.86 percentage points
Rotational augmentation provides stable improvement: +3.78 percentage points Synergistic effect of both techniques: total improvement of 8.44 percentage points
GRCR-Net

## Slide 20: Performance Across Different SNR Conditions
GPR Denoising Performance Analysis
-20
-15
-10
10
15
-5 0 5
Signal-to-Noise Ratio (dB)
0
20
40
60
80
100
Classification Accuracy (%)
-10dB
0dB
10dB
Model Performance vs SNR
ResNet CNN1D
ComplexCNN
Hybrid Hybrid+GPR+Aug
-20.0
-17.5
-15.0
-5.0
-2.5
-12.5 -10.0 -7.5
Signal-to-Noise Ratio (dB)
0
5
10
15
20
25
30
35
40
Classification Accuracy (%)
Low SNR Performance Detailed Comparison
ResNet CNN1D
ComplexCNN
Hybrid
Hybrid+GPR+Aug
GRCR-Net

## Slide 21: Detailed SNR Performance Analysis
SNR | Base | +GPR | Gain
-20 | 8.93 | 9.96 | +1.03
-18 | 8.68 | 10.22 | +1.54
-16 | 9.85 | 12.69 | +2.84
-14 | 11.08 | 17.32 | +6.24
-12 | 12.65 | 24.18 | +11.53
-10 | 20.15 | 35.05 | +14.90
-8 | 34.66 | 47.36 | +12.70
-6 | 54.86 | 61.21 | +6.35
-4 | 64.02 | 70.84 | +6.82
-2 | 75.66 | 80.89 | +5.23
0 | 79.43 | 83.17 | +3.74
2 | 82.96 | 87.07 | +4.11
4 | 84.56 | 89.00 | +4.44
6 | 83.93 | 89.38 | +5.45
8 | 83.17 | 89.10 | +5.93
10 | 84.73 | 89.85 | +5.12
12 | 85.81 | 90.31 | +4.50
14 | 85.31 | 88.81 | +3.50
16 | 82.25 | 88.15 | +5.90
18 | 83.87 | 88.98 | +5.11
Key Findings:
Low SNR (-20 to -8dB):
Peak: +14.90% at -10dB Average: 7.25%
Medium SNR (-6 to 4dB):
Range: 3.74% to 6.82%
Average: 5.12%
High SNR (6 to 18dB):
Range: 3.50% to 5.93%
Average: 5.07%
Best Performance:
+14.90% improvement
GRCR-Net

## Slide 22: Training Convergence Analysis
20
40
80
100
60
Training Epochs
0.00
0
0.10
0.20
0.30
0.40
0.50
0.60
0.70
Validation Accuracy
Validation Accuracy Convergence Curves
CNN2D CNN1D
Transformer ResNet
Complex NN Hybrid
GRCR-Net (Proposed)
Key Insights:
Fast Convergence: Optimal in 5-10 epochs
Stable Training: Smooth without oscillations
Best Performance: Outperforms all baselines
Robust Results: Consistent across runs
Training Advantage: Fast & Stable Convergence
GRCR-Net

## Slide 23: Major Technical Contributions
1
2
3
Adaptive Noise Suppression Technology
First SNR-adaptive GPR denoising algorithm Optimal denoising under different noise conditions
Novel approach for complex electromagnetic environments
Geometric Property Data Augmentation Strategy Exploits inherent symmetry of modulation signals Significantly improves robustness to phase offset Effective solution for data-scarce scenarios
Hybrid Neural Network Architecture Innovation First fusion of ComplexCNN and ResNet advantages Deep residual learning in complex domain
New architectural paradigm for I/Q signal processing
GRCR-Net

## Slide 24: Comparison with State-of-the-Art Methods
Method | Accuracy(%) | Year | Publication | Model Size | Key Technology
LDCVNN | 62.41 | 2025 | JCR Q2 | Lightweight | Dual-branch complex network
ULCNN | 62.47 | 2022 | JCR Q2 | Lightweight | Ultra-lightweight CNN
AMC-NET | 62.51 | 2023 | ICASSP (CCF B) | Normal | Frequency-domain denoising
HFECNET-CA | 63.92 | 2023 | JCR Q2 | Lightweight | Attention mechanism
AbFTNet (Previous SOTA) | 64.59 | 2024 | JCR Q2 | Normal | Multimodal fusion
GRCR-Net (Ours) | 65.38 | 2025 | This Work | Lightweight | GPR+Rotation+Hybrid
Core Advantages:
Performance Leadership: Surpasses best existing method by 0.79% Technical Innovation: Organic fusion of three core technologies Practical Robustness: Stable performance in complex environments Scalability: Components can be applied independently
GRCR-Net

## Slide 25: Comprehensive Performance Comparison
SOTA Achievement: 65.38% accuracy
+0.79% vs. AbFTNet (2024)
+2.87% vs. AMC-NET (2023)
+2.91% vs. ULCNN (2022)
Key Advantages:
Clear performance leadership Consistent improvements Robust across conditions New benchmark established
New SOTA 65.38%
GRCR-Net

## Slide 26: Research Summary
GRCR-Net: A Breakthrough AMC Method
Core Achievements:
Achieved 65.38% classification accuracy
Surpassed existing SOTA methods
Exceptional performance in low SNR environments
Proposed three core technical innovations
Technical Breakthroughs:
Adaptive GPR denoising algorithm
Geometric symmetry data augmentation
Hybrid ComplexCNN-ResNet architecture
Impact Significance:
Solution for complex electromagnetic environments
Advancement of cognitive radio technology
New insights for signal processing field
Important theoretical and practical value
Open Source Contribution:
Complete code open-sourced
Detailed experimental data
Comprehensive technical documentation
GRCR-Net

## Slide 27: Future Research Directions
1
2
3
Algorithm Optimization and Extension
Explore performance in more complex channel environments Research real-time processing optimization strategies Extend to more modulation types
Technology Fusion and Innovation
Combine with emerging architectures like Transformers Explore multimodal signal fusion
Research self-supervised learning methods
Practical Deployment and Applications
Hardware acceleration and edge computing optimization Large-scale real-environment validation
Industrial application promotion
GRCR-Net

## Slide 28: Thank You!
GRCR-Net
Questions and Discussion Welcome
Open Source Repository:
https://github.com/LJK666666666/radioML-v3